## Slide 1
CardioScan AI
ECG Arrhythmia Detection System
Project Presentation • B.Tech CSE (AI/ML) • Semester 4
Aman Kumar • Krish Astwal • Kenis Surat Ningombam • Aryan Singh
1

## Slide 2
1. Problem & Motivation
Why automated ECG beat classification matters
• ECG analysis is a structured time-series classification problem with substantial morphology variation and signal noise.
• CardioScan is designed as an academic end-to-end prototype: preprocessing → CNN → API → browser visualization.
• The project focuses on five AAMI-oriented beat classes rather than full clinical ECG diagnosis.
2

## Slide 3
2. ECG & AAMI-Oriented Classes
Beat-level classification target
• N — Normal
• S — Supraventricular ectopic
• V — Ventricular ectopic
• F — Fusion
• Q — Unknown / unclassifiable
• Training labels are derived from MIT-BIH annotations using the corrected mapping implemented in data_preprocessing.py.
3

## Slide 4
3. Dataset
MIT-BIH Arrhythmia Database
• 48 half-hour two-channel ambulatory ECG recordings from 47 subjects.
• Sampling frequency: 360 samples/second.
• Main processing path uses the first channel (MLII).
• Expert .atr annotations provide training-time beat locations and labels.
• Raw database files are not redistributed in the GitHub repository; the preprocessing script downloads them through WFDB.
4

## Slide 5
4. Signal Processing Pipeline
From raw ECG to model-ready beat
• 1. Read WFDB record and select the ECG channel.
• 2. Fourth-order Butterworth bandpass filter: 0.5–45 Hz.
• 3. Training: use annotation R-peak locations. Inference: derivative-squared + moving-average detector.
• 4. Extract 200 ms before + 380 ms after each peak.
• 5. Pad/truncate to 280 samples.
• 6. Apply per-beat Z-score normalization.
5

## Slide 6
5. Model Architecture
1D residual-style CNN
• Input: 280 × 1 ECG beat.
• Conv1D stem: 32 filters, kernel 7, BatchNorm, ReLU, MaxPool.
• Residual blocks: 64 / 128 / 256 filters with dilations 1 / 2 / 4.
• Global Average Pooling → Dense(128) → Dropout(0.4) → Softmax(5).
• Corrected parameter count: approximately 530,373 trainable parameters.
6

## Slide 7
6. Training Configuration
Reproducible training setup
• Loss: sparse categorical cross-entropy.
• Optimizer: Adam; initial learning rate 1e-3 with CosineDecayRestarts.
• Batch size: 128; maximum 60 epochs.
• Early stopping: patience 10, restore best weights.
• Balanced class weights address severe class imbalance.
• Stratified beat-level split: approximately 70% train / 15% validation / 15% test.
7

## Slide 8
7. Results
Reported performance on the supplied held-out test set
• Test accuracy: 98.95%
• Macro F1: 96.91%
• Weighted F1: 98.96%
• Per-class F1: N 1.00 • S 0.98 • V 0.98 • F 0.90 • Q 1.00
• Fusion is the most difficult reported class.
8

## Slide 9
8. Evaluation Caveat
What the 98.95% result does — and does not — mean
• The split is performed at beat level, not by patient.
• Beats from the same patient can therefore appear in training and test partitions.
• The result is not patient-independent validation and should not be presented as clinical validation.
• Future evaluation should use subject-disjoint protocols such as DS1/DS2 or an independent dataset.
9

## Slide 10
9. Full-Stack System
React + Flask + TensorFlow/Keras
• React/Vite frontend: upload matching .dat + .hea files and visualize results.
• Flask API: POST /api/analyze and GET /api/health.
• WFDB + SciPy + NumPy: signal reading and preprocessing.
• TensorFlow/Keras model: five-class probability output.
• Temporary upload directory prevents persistent storage of submitted files.
10

## Slide 11
10. Limitations & Future Work
Research prototype scope
• Current model is trained on a single benchmark database.
• Main path uses a single ECG channel and 360 Hz-oriented preprocessing.
• No prospective clinical validation has been performed.
• Future: patient-independent evaluation, multi-lead ECG, streaming inference, transformers, signal-quality checks, calibration, and external clinical validation.
11

## Slide 12
11. Conclusion
CardioScan AI
• End-to-end ECG beat classification research prototype.
• 98.95% accuracy and 96.91% macro F1 on the supplied beat-level stratified test split.
• Corrected documentation now distinguishes benchmark performance from patient-independent and clinical validation.
• Academic prototype only — not a medical device or diagnostic system.
12